# Units
Sizes and coordinates are given in mils (1/1000 inch)
# Heading
Format :
EESchema Schematic File Version 1
LIBS: libraries list (not used, for information only).
EELAYER nn mm (nn mm not used, reserved)
EELAYER END
$Descr Sheet size dimx dimy (sheet size = A4..A0 ou A..E)
Title block description (Texts of the title block)
$EndDescr

EESchema Schematic Spins Version 1
LIBS:brooktre, cypress, ttl, power, linear, memory, xilinx, idiot, aaci, INTEL, special, device, dsp
EELAYER 20 0
EELAYER END
$Descr A3 16535 11700
Sheet 1 4
""
Date “28 DEC 1996”
Rev ""
Comp ""
Comment1 ""
Comment2 ""
Comment3 ""
Comment4 ""
$EndDescr

# Description of a component
Format:
$Comp
L name reference
U N mm time_stamp
P posx posy
List of fields:
F field_number “text” orientation posX posY size Flags (see below)
1 posx posy (redundant: not used)
A B C B ( orientation matrix with A, B, C, D = - 1, 0 or 1)
$EndComp
Description of the fields:
F n “text” orientation posx posy dimension flags
with n = field number (reference field = 0, value field = 1, N = 0..11)
orientation = H (horizontal) or V (vertical).
Example:

Comp
L CONN_3 JP3
U 1 1 329879E1
P 1200 2000
F 0 “JP3” H 1250 2200 60 0000
F 1 “CONN_3” V 1350 2000 50 0000
1 1200 2000
- 1 0 0 - 1
$EndComp

# Description of a NoConnect symbol
Format: NoConn ~ posx posy
Example:
NoConn ~ 13400 5500

# Description of a hierarchical sheet symbol
Format:
$Sheet
S posx posy dimx dimy
List of Sheet Labels
$EndSheet
Format of Sheet Labels
Fn “text” forms side posx posy dimension
With:
n = sequence number (0..x).
n = 0: name of the corresponding schematic file.
n = 1: name of the sheet of hierarchy.
form = I (input) O (output)
side = R (right) or L (left).
Example:

$Sheet
S 1800 1600 1500 1500
F0 “PROGALIM.SCH” 60
F1 “PROGALIM.SCH” 60
F2 “CLK” O R 3300 1800 60
F3 “/RESET” O R 3300 2000 60
F4 “VPWR” O R 3300 2700 60
F5 “/HALT” O R 3300 2100 60
F6 “TRANSF1” I L 1800 1900 60
F7 “TRANSF2” I L 1800 2000 60
F8 “3.84MH” O R 3300 2200 60
$EndSheet

# Description of a text note
Format: Text Notes posx posy orientation dimension ~
Text
Example:
Text Notes 2100 3250 1 60 ~
TOTO

# Description of a Global Label
Format: Text GLabel posx posy orientation dimension shape
Text
Example:

Text GLabel 3100 2500 2 60 UnSpc
TITI
Text GLabel 3150 2700 1 60 3State
3STATES
Text GLabel 2750 2800 0 60 UnSpc
BIDI
Text GLabel 2750 2650 0 60 Output
GLABELOUT
Text GLabel 2750 2400 0 60 Input
RESET

# Description of a label
Format: Text Label posx posy orientation dimension ~
Text
Example:

Text Label 3400 2000 0 60 ~
/RESET

# Description of a junction
Format: Connection ~ posx posy
Example:

Connection ~ 13300 6500

# Description of a wire segment (Wire)
Format:
Wire Wire Line
startx starty endx endy
Example:

Wire Wire Line
3300 1800 3900 1800

# Description of a Bus segment
Format:
Wire Bus Line
startx starty endx endy
Example:

Wire Bus Line
3900 5300 4500 5300

# Description of a dotted line segment
Format:
Wire Notes Line
startx starty endx endy
Example:

Wire Notes Line
2850 3350 2850 3050

# Description of a bus entry
Format:
For an entry wire/bus :
Wire Wire Bus
startx starty endx endy
For an entry bus/bus :
Wire Bus Bus
startx starty endx endy
Example:

Entry Wire Bus
4100 2300 4200 2400
Entry Bus Bus
4400 2600 4500 2700