Board File Format
# General Informations:
Board file ( *.brd files ) are in ascii format.
Dimensions are in 1/10000 inch, except for the page size (in 1/1000 inch).
First line is something as:
PCBNEW-BOARD Version 0 date 5/1/2005-14:45:23
All the following descriptions are like this:
$DESCRIPTION
some data
...
$endDESCRIPTION
Example:
$GENERAL
Ly 1FFF8001
Links 66
NoConn 0
Di 24940 20675 73708 40323
Ndraw 16
Ntrack 267
Nzone 1929
Nmodule 29
Nnets 26
$EndGENERAL
$SHEETDESCR
Sheet A4 11700 8267
Title ""
Date "23 feb 2004"
Rev ""
Comp ""
Comment1 ""
Comment2 ""
Comment3 ""
Comment4 ""
$EndSHEETDESCR
# Layer numbering:
Tracks and other items (texts, drawings ...) use one layer.
Pads and vias use several layers.
There are 16 copper layers and 12 technical layers.
The layer parametre used in descriptions has the value:
value layer name / 0 Copper layer / 1 to 14 Inner layers / 15 Component layer	"Copper" layers
16 Copper side adhesive layer / 17 Component side adhesive layer / 18 Copper side Solder paste layer / 19 Component Solder paste layer / 20 Copper side Silk screen layer / 21 Component Silk screen layer / 22 Copper side Solder mask layer / 23 Component Solder mask layer / 24 Draw layer (Used for general drawings) / 25 Comment layer (Other layer used for general drawings) / 26 ECO1 layer (Other layer used for general drawings) / 26 ECO2 layer (Other layer used for general drawings) / 27 Edge layer. Items on Edge layer are seen on all layers	Technical layers

Mask layer:
Sometimes, a mask layer parameter is used.
It is a 32 bits mask used to indicate a layer group usage (0 up to 32 layers).
A mask layer parameter is given in hexadecimal form.
Bit 0 is the copper layer, bit 1 is the inner 1 layer, and so on...(Bit 27 is the Edge layer).
Mask layer is the ORed mask of the used layers

# First line of description:
Format:
PCBNEW-BOARD Version <version number> date <date>-<time>
Date and time are useful only for information (not used by pcbnew).

# $GENERAL
This data is useful only when loading file.
It is used by pcbnew for displaying activity when loading data.
$GENERAL	Start description
Ly 1FFF8001	Obsolete (used for old pcbnew compatibility)
Links 66	Total number of connections
NoConn 0	Remaining connections
Di 24940 20675 73708 40323	Bounding box coordinates: / X_start Y_start X_end Y_end
Ndraw 16	Number of draw items like eged segments, texts...
Ntrack 267	Number of track segments
Nzone 1929	Number of zone segments
Nmodule 29	Number of modulss
Nnets 26	Number of nets
$EndGENERAL	End description

# $SHEETDESCR
This the page size and texts.
$SHEETDESCR	Start description
Sheet A4 11700 8267	<Page size> X_size Y_size in mils (1/1000 inch)
Title ""	Title text
Date "23 feb 2004"	Date text
Rev ""	Revision text
Comp ""	Company name text
Comment1 ""	Comment text, line 1
Comment2 ""	Comment text, line 2
Comment3 ""	Comment text, line 3
Comment4 ""	Comment text, line 4
$EndSHEETDESCR	End description

# $SETUP block:
This data bock is used for design settings
This is useful only for board edition.
$SETUP	Start block "SETUP"
InternalUnit 0.000100 INCH	Internal unit for pcbnew, all coordinates are in / this unit
GridSize 500 500	Current grid X Y size (500 x 500 units)
ZoneGridSize 100	Grid used for zone filling (100 units, i.e 0.01 inch)
Layers 2	Number of layers (2 = double sided board) / must be 1 to 16
TrackWidth 250	Current track width
TrackWidthHistory 170 / TrackWidthHistory 250 / TrackWidthHistory 400	Last used track widths
TrackClearence 100	Isolation for DRC (Design rules check)
ZoneClearence 200	Isolation used in zone filling
DrawSegmWidth 120	Current segment width for drawings on technical layers
EdgeSegmWidth 120	Current segment width for drawings on "edge layer"
ViaSize 700	Current via size
ViaDrill 250	Via drill for this board
ViaSizeHistory 450 / ViaSizeHistory 650 / ViaSizeHistory 700	Last used via sizes
TextPcbWidth 120	Current text width for texts on copper or technical layers. This is not for text on footprints
TextPcbSize 600 600	Current text X Y size
EdgeModWidth 120	Current Segment width for footprint edition
TextModSize 120 600	Current text XY size for texts for footprint edition
TextModWidth 120	Current text width for texts for footprint edition
PadSize 700 700	Current X Y pad size (footprint edition)
PadDrill 320	Current pad drill
AuxiliaryAxisOrg 0 0	Auxiliary axis position / (Auxiliary axis is the reference coordinate (0 0 coordinate) for EXCELLON drilling files
$EndSETUP	End block "SETUP"

# $EQUIPOT
$EQUIPOT describes a net name.
$EQUIPOT	Start block
Na 2 "N-000026"	Na <internal net number> « net name »
St ~
$EndEQUIPOT	End block

Note1:
Internal net number is an arbitrary number.
It is computed by pcbnew when compiling netlist.
Note2:
Net 0 is not a real net.
Net 0 is the net number used internally by pcbnew for all the no connected pads.

Example:
$EQUIPOT;
Na 0 ""
St ~
$EndEQUIPOT$EQUIPOT
Na 1 "DONE"
St ~
$EndEQUIPOT
$EQUIPOT
Na 2 "N-000026"
St ~
$EndEQUIPOT
$EQUIPOT
Na 3 "TD0/PROG"
St ~
$EndEQUIPOT
# $MODULE
Decription =start by:
$MODULE <module name>
And ends with
$EndMODULE <module name>
Module description has four sections:
1. General description (fixed size)
2. Field description (variable size)
3. Drawing description (variable size)
4. Pad description. (variable size)
5. 3D shape informations.
Note:
All coordinates are relative to the module position.
Its means the coordinates of segments, pads, texts ... are given for a module in position 0, rotation 0.
If a module is rotated or mirrored, real coordinates must be computed according to the real position and rotation.
## General description:
$MODULE bornier6	$MODULE <module lib name>
Po 62000 30500 2700 15 3EC0C28A 3EBF830C ~~	Po Xpos Ypos Orientation(0.1deg) Layer TimeStamp Attribut1Attribut2 / Attribut1 = ~or 'F' for autoplace (F = Fixed, ~= moveable) / Attribut2 = ~or 'P' for autoplace (P = autoplaced)
Li bornier6	Li <module lib name>
Cd Bornier d'alimentation 4 pins	Cd comment description (displayed when browsing libraries)
Kw DEV	Kw Keyword1 Keyword2 ... (for footprint selection by keywords)
Sc 3EBF830C	Sc TimeStampOp
Op 0 0 0	Op <rotation cost 90 deg> <rotation cost 180 deg> for auto place. / rotation cost = 0 (no rotation allowed) to 10 (null cost)

Note:
Usually, components are on layer 15 (component layer) or 0 (copper layer).
If the component is on layer 0, it is"mirrored". The "mirror axis is the X axis
## Field Description:
There are 2 to 12 fields
Field 0 = component reference (U1, R5 ...) (required)
Field 1 = component value (10K, 74LS02 ...) (required)
Other fields (optional) are comments.
Format:
T<field number> Xpos Ypos Xsize Ysize "text"

T0 500 -3000 1030 629 2700 120 N V 21 "P1"	Xpos Ypos Xsize Ysize "text" / T0 = reference
T1 0 3000 1201 825 2700 120 N V 21 "CONN_6"	T1 = value

## Drawings:
Tells how to draw module shape.
Drawings are segment, circle, arc.
DS -6000 -1500 -6000 1500 120 21	DS is a Draw Segment / DS Xstart Ystart Xend Yend Width Layer
DS 6000 1500 6000 -1500 120 21	An other Draw Segment

Other Drawings are:
DC ox oy fx fy w	DC is a Draw Circle / DC Xcentre Ycentre Xpoint Ypoint Width Layer
DA x0 y0 x1 y1 angle width layer	DA is a Draw Arc / X0,y0 = Start point x1,y1 = end point

## Pad Descritions:
All the pads of this footprint are listed here (Many $PAD/$EndPAD sections here)..
See $PAD description.
## $SHAPE3D
3D shape informations:
The real shape description is a vrml file, build by Wings3d.
This shape can be scaled, moved and rotated.
This is because a single 3D shape can be used for many footprints (for instance, we use the shape resistor.wrl for several resistor footprints, by tuning the X, Y, Z scale of the 3D shape according to the different size of resistor footprints).
Some smd footprints are using this feature.
For the same reasons, the 3D shape can be moved (by the move factor) and/or rotated.
Real shape unit is 0.1 inch (1 unit vrml = 0.1 inch = 2.54 millimeter).
An other reason exists: when a footprint is very big ( a big connector) or very small (a small SMD resitor) whe must create a 3D shape small or bigger than real size, in order to use easily the 3D modeler.

$SHAPE3D	Start description
Na "device/bornier_6.wrl"	FileName (default path is kicad/modules/packages3d/)
Sc 1.000000 1.000000 1.000000	X Y Z scale factor
Of 0.000000 0.000000 0.000000	X Y Z offset (move vector, in 3D units (0.1 inch))
Ro 0.000000 0.000000 0.000000	X Y Z rotation (in degree)
$EndSHAPE3D	End description

The 3D shape coordinates are relative to the footprint coordinates.
The 3D shape must be scale, moved and rotated according to the parameters Sc Of and Ro,
and after moved and rotated according to the footprint coordinates and rotation.
If the footprint is « inverted » (that is, located on copper side) the 3D shape must be « inverted » too.
Note:
A footprint may have several 3D shapes (for instance an integrated circuit and his socket).

# $PAD
Pads have different shapes and attributes.
Pad shapes are:
Circle.
Oblong(or oval).
Rectangular (Square is like a rectangle).
Trapeze.
Pad attributes are:
- Normal (Has usualy a hole)
- Smd (used for Surface Mounted Devices). Has no hole.
- Connector (used for connectors like a PC Board Bus connector)
- Mechanical. (Like a hole for mechanical use)
And shape can be draw with an offset related to the drilling hole.
The hole shale is round or oblong
$PAD	Start description
Sh "2" C 1500 1500 0 0 2700	Shape: <pad name> shape Xsize Ysize Xdelta Ydelta Orientation
Dr 600 0 0 / or (oblong hole) / Dr 600 0 0 O 600 650	Drill <Pad drill> Xoffset Yoffset (round hole) / or (oblong hole) / Drill <Pad drill.x> Xoffset Yoffset <Hole shape> <Pad drill.x> <Pad drill.y>
At STD N 00E0FFFF	Attributs: <Pad type> N <layer mask>
Ne 8 "GND"	Net reference of the pad: <netnumber> <net name>
Po -3000 0	X_pos Y_pos (relative to the module position)
$EndPAD	End description

Note:
<Pad type> is the Pad Attribute. It is one of: "STD" "SMD" "CONN" "HOLE" "MECA".
Shape is one of:
- C (circle)
- R (Rectangular).
- O (Oblong)
- T (Trapèze)
Hole shape = O (O for Oblong)

Example:
$PAD
Sh "3" C 1500 1500 0 0 2700
Dr 600 0 0
At STD N 00E0FFFF
Ne 10 "TD0_1"
Po -1000 0
$EndPAD
# Graphic items:
There are drawing items like segments, circles, texts, targets and cotations.
## $DRAWSEGMENT
Draw segments are :
- segments (strait line)
- circles
- arcs
### Line:
$DRAWSEGMENT	Start description
Po 0 67500 39000 65500 39000 120	Position shape Xstart Ystart Xend Yend width
De 28 0 900 0 0	Description layer type angle timestamp status
$EndDRAWSEGMENT	End description

Note:
- shape = 0
- Angle is used only for arc segments (unused for line, left for compatibility).
### Circle:
$DRAWSEGMENT	Start description
Po 1 67500 39000 65500 39000 120	Position shape Xcentre Ycentre Xend Yend width
De 28 0 900 0 0	Description layer type angle timestamp status
$EndDRAWSEGMENT	End description

Note:
- shape = 1
- Angle is used only for arc segments (unused for circle, left for compatibility).
- End is a point of this circle. (If Xend or Yend is 0, the other coordinate is the radius)
### Arc:
$DRAWSEGMENT	Start description
Po 2 67500 39000 65500 39000 120	Position shape Xstart Ystart Xend Yend width
De 28 0 900 0 0	Description layer type angle timestamp status
$EndDRAWSEGMENT	End description

Note:
- shape = 2
- start and end are the 2 points of the arc. angle is the arc angle (in 0.1 degree). Center coordinates are computed by pcbnew from start, end and angle.
Currently, only 90 degrees arcs are supported.(thereby, angle = 900)
Example:
$DRAWSEGMENT
Po 0 67500 34000 67500 39000 120
De 28 0 900 0 0
$EndDRAWSEGMENT
## $TEXTPCB
Example:
$TEXTPCB	Start description
Te "TDI"	Text "string"
Po 57250 35750 600 600 150 0	Position Xstart Ystart Xsize Ysize rotation
De 15 1 0 0	Description layer normal timestamp 0 / normal = 0 : text is mirrored. / normal = 1 : text is normal.
$EndTEXTPCB	End description

Example:
$TEXTPCB
Te "TCK"
Po 57250 33500 600 600 150 0
De 15 1 0 0
$EndTEXTPCB
## $MIRE
shape 1
shape 0

$MIREPCB	Start description
Po 0 28 28000 51000 5000 150 00000000	Position shape Xpos Ypos size width timestamp
$EndMIREPCB	End description

## $COTATION

$COTATION	Start description
Ge 0 24 0	General shape layer timestamp / currently, shape = 0.
Te "4,5500''"	Text "string" / string is the cotation value in inches ou millimetres
Po 50250 5791 600 800 170 0 1	Position (for text) Xpos Ypos Xsize Ysize width orient normal
Sb 0 27500 6501 73000 6501 150 / Sd 0 73000 9000 73000 5081 150 / Sg 0 27500 9000 27500 5081 150 / S1 0 73000 6501 72557 6731 150 / S2 0 73000 6501 72557 6271 150 / S3 0 27500 6501 27943 6731 150 / S4 0 27500 6501 27943 6271 150	Coordinates of segments (axis, arrows...)
$EndCOTATION	End description

# Track, vias and Zone section:
## $TRACK
Track section decribes tracks and vias on copper layers.
Each track (or via) has a two line descrition:
For a track segment:
Position shape Xstart Ystart Xend Yend width
Description layer 0 netcode timestamp status
Shape parameter is set to 0 (reserved for future changes).
For a via:
Position shape Xstart Ystart Xend Yend diameter
Description layer 1 netcode timestamp status
For a via, layer parameter gives :
On the 4 less significant bits: the starting layer of the via
On the 4 next bits: the ending layer.
For instance, a via starting at copper kayer (layer 0) end ending at component layer (layer 15 has the layer parametre set to F0 hexadecimal or 240 decimal.
Shape parameter is the via type (through = 3, blind = 2, buried = 1)
Timestamp parameters are set to 0 (reserved for future changes).
Status parameter can be set to 0 (Used internally for routing infos)..

$TRACK	Start description
Po 0 36750 37000 36550 37000 250	Position shape Xstart Ystart Xend Yend width / width = diameter for a via
De 15 0 1 0 400	Description layer type netcode timestamp status / type = 0 for a track segment. / type = 1 for a via
Po 0 39000 36750 38750 37000 250 / De 15 0 1 0 0	An other track
Po 3 53500 27000 53500 27000 650 / De 15 1 14 0 0	This is a via (via "through") from layer 15 (component) to layer 0 (copper)
$EndTRACK	End description

## $ZONE
Zone section is like track section. (There is no via in Zone section).
$ZONE	Start description
Po 0 67100 33700 67100 38600 100 / De 0 0 2 3EDDB09D 0	Same as track description
$EndZONE	End description

# $EndBOARD
$EndBOARD terminates the whole board description.
Must be the last line.