Notes about Pcbnew new file format and its internal data

This is only some notes and not an “official guideline”.
I tried to summarize ideas and guidelines found in a lot of mails about this topic
J-P Charras
# File format syntax:
Based on the Specctra syntax (but not necessary the file format).
- All tokens should be lowercase.
- There will be user defined
Strings such as board text and copper layer names which will have upper case characters, but these will typically be quoted.
## Guidelines for data representation:
### Coordinates:
Coordinates should coordinates be relative to the origin of their containing object
Generally speaking, data in files must give properties and never the internal coding used in Kicad
Specially internal units, internal angles units.
TODO: Y axis orientation ?:
Prefered: use the usual Y axis orientation instead of the reverse Y screen orientation (like now).
Most of file formats use the usual Y axis orientation.
### Engineering units: Coordinates representation in file:
It is very desirable to avoid exponential floating point values in the file, and instead have a presentation like "xxx.yyy" or "0.0x" or "0.x", or even "xy".

Values like 4e-2 are not as easy for a human to read, so do not use them.

I (<Dick>) suggest that initially the distance engineering units used in a new board file be mils or deci-mils. Let's first consider mils:

In mil mode, to show deci-mils or centi-mils you would show a value like 0.4 or 0.04 respectively.
To show a value of 20 inches you would show a value of 20000 and would need no decimal point in that value.
Note that in mil mode we are not really limiting the resolution to mils. It simply controls where the decimal point is.

Now let's consider deci-mils:
In deci-mil mode, to show decimils or centimils you would show a value like 4 or 0.4 respectively.
To show a value of 20 inches you would show a value of 200000.

The format string I found best for outputting numbers in this range is the "%.6g".
It eliminates the exponent where possible, and the decimal point where possible.
In fact I am not sure that the DSNLEXER knows much about a number with an exponent in it, so we should avoid this if we can.
Mil mode may be one of the better options.

Board files should be identified with the engineering units used, this way alternative units can be used in the future.
See the Specctra unit and resolution descriptors for more ideas.

Initially I am not expecting that the new board file format changes the internal units in memory at all, but it provides a pathway for such a change in the future.
That is for now, the coordinates remain integers, and their interpretation remains the same.
To work scope to change the internal units in the future is approximately cut in half by the new file format.
## Keywords;
Use only basic ascii codes ( Letters (lower case only) and digits)
## Strings:
Used in fields and comments
- Use quoted notation like "this is a sample"
- Can contain a quote like "this is a ""sample""" or "this is a \"sample\""
- Support extended codesets (unicode ?)
- Include multi-line strings like "line 1\nline 2" or "line 1\0Aline 2"
# Ideas for layers handling:
<Dick notes>: I think if we introduce a new class (hierarchy?) called LAYERSET we can hide the details of how the IsOnLayer() method is done, along with the hiding the data that is used in that test.
So BOARD_ITEM:: IsOnLayer( aLayerNumber ) would then call LAYERSET::IsOnLayer () to do its work, and the LAYERSET data would be hidden inside itself.
This way we can support a number of different types of layerset specifications, including but not limited to: list, range, and all copper layers.
The problem with using "list of layers" to also indicate "all layers" is that this becomes a layer count dependent test.
Same for range. Whereas if we have a special flag for the "all copper layers" case in the encapsulated data of LAYERSET, then we can handle both situations.
A LAYERSET element would become part of a D_PAD element.
And would have its own textual representation when being serialized to a file. The textual representation could be dropped into the current location for layermask for D_PADs in your existing *.brd file format.

Examples of a textual representations for LAYERSET specs (range, list, and all) would be:

(layer_range 0 4 )	a range
(layers 0 1 2)	a layer list of arbitrary length
(layers all)	all layers
(layers front back)	a list, but with special layer names
(layers front)	front only
(layers back)	back only

# Layers capacity
If a bitmap is used to handle layers info in pads or others items, the bitmap could be a long long integer.
Therefore 64 layers could be handled:
Copper layers 48
Technical layers 16

# Proposed layers names keywords or fixed names
Front	first layer seen
<todo>	inners layers
back	last layer seen
soldp_fr	solder paste (front side)
soldp_bk	solder paste (back side)
silks_fr	silkscreen (front side)
silks_bk	silkscreen (back side)

# Layers numbering (internal use ?)
assuming we have <copper_layer_ count> copper layers:

front	0
inner1	1
…	...
inner<n>	<copper_layer_ count>-2
back	<copper_layer_ count>-1

# Single sided boards:
Have one front layer or one back layer.
Some have a front layer plus a copper plane on back (microwaves applications).
Do we use always a double sided board ( do not support one layer) and have the second layer disabled ?